## Slide 1: Analysis of functional groups in atmospheric aerosols by infrared spectroscopy: ElnetPLS model
Matteo Reggente
Giulia Ruggeri
Adele Kuzmiakova
Satoshi Takahama
Swiss Federal Institute of Technology Lausanne
Ann Dillner
University of California, Davis

## Slide 2: Nutshell
What: FT-IR analysis of ambient sample collected on Teflon filters.
Why:
  Reduce the operating costs of large air quality monitoring networks and field campaigns.
  Associate molecular structure to other aerosol measurements.
How: Statistical modeling, to retrieve relevant information.
  ElnetPLS model.
Results from the IMPROVE network (US).
Nutshell
1/1

## Slide 3: Background

## Slide 4: FT-IR spectroscopy
Measures absorption due to net change in dipole moment of vibrating/rotating molecules
Absorption is linearly related to abundance of a substance
Relatively inexpensive to own and operate
Requires advanced algorithms to process spectral information
FTIR spectrometer
Background
1/7

## Slide 5: Data: Teflon/quartz filters collected in the IMPROVE network
3136 collocated ambient PM2.5 samples:
PTFE filters for FT-IR spectra analysis
Quartz filters for TOR OC
18 sites:
7 sites 2011
17 sites 2013
Dillner A. M. and Takahama S., AMT, 8, 1097-1109, 2015
Dillner A. M. and Takahama S., AMT, 8, 4013-4023, 2015
Reggente et al., AMT, 9, 441-454, 2016
Takahama et al., AMT, 9, 3429-3454, 2016
Kuzmiakova et al. AMT, 9, 2615-2631
Background
2/7

## Slide 6: Data - Collection
Background
3/7

## Slide 7: Data – Baseline correction
Teflon
scattering
Teflon
peak absorbance
Background
4/7

## Slide 8: Data – Baseline correction
Kuzmiakova et al. AMT, 9, 2615-2631
Teflon
scattering
Teflon
peak absorbance
Background
4/7

## Slide 9: Organic aerosols
Organic aerosols have many different sources
Complex mixtures of 10,000+ compounds
Carbon content commonly analyzed by thermal optical methods
Background
5/7

## Slide 10: Organic aerosols
quantification
Background
6/7

## Slide 11: ElnetPLS algorithm
GOAL: identify the most relevant infrared absorption bands that allow us to make quantitative predictions of TOR OC using FT-IR spectra
HOW: ?
Background
7/7

## Slide 12: ElnetPLS algorithm
GOAL: identify the most relevant infrared absorption bands that allow us to make quantitative predictions of TOR OC using FT-IR spectra
HOW: Elastic net regularization
Background
7/7
Notes: RSS: least square problem. Residual sum of squares
Lasso: sparseness constraints
Ridge: restrictions on the overall size of the regression vector

## Slide 13: ElnetPLS algorithm
GOAL: identify the most relevant infrared absorption bands that allow us to make quantitative predictions of TOR OC using FT-IR spectra
HOW: Elastic net regularization and partial least square (PLS) regression
Background
7/7
Notes: RSS: least square problem. Residual sum of squares
Lasso: sparseness constraints
Ridge: restrictions on the overall size of the regression vector

## Slide 14: Results

## Slide 15: TOR OC prediction, Full Spectra
Results
1/11
Dillner A. M. and Takahama S., AMT, 8, 1097-1109, 2015
Reggente et al., AMT, 9, 441-454, 2016

## Slide 16: ElnetPLS model – Wavenumbers selected
anhydride
aldehyde
ketone
carboxylic acid
10 Wavenumbers selected (blue vertical lines)
Results
2/11

## Slide 17: TOR OC prediction, Full Spectra Vs. ElnetPLS model
Results
3/11
Full Spectra
10 wavenumbers

## Slide 18: TOR OC prediction, Full Spectra Vs. ElnetPLS model
Results
3/11
Full Spectra
10 wavenumbers

## Slide 19: TOR OC prediction, Full Spectra Vs. ElnetPLS model
Results
3/11
Full Spectra
10 wavenumbers

## Slide 20: TOR OC prediction, Calibration 2011 – Test 2013 Addl
Results
4/11
Full spectra
(box denotes
calibration range)
10 wavenumbers
Using only the original set of samples, eliminate uninformative wavelengths that interfere with predictions.

## Slide 21: Past studies: aCH
Past studies (e.g. ) show that alkane CH (aCH) should contribute a significant amount of OM mass fraction
Ruthenburg et al. , Atmos. Environ., 86, 46-57, 2014
Results
6/11
IMPROVE 2011, 6 sites

## Slide 22: aCH Vs. ElnetPLS wavenumbers
Results
7/11
aCH
aCH
carbonyl

## Slide 23: Why can we predict aCH?
Why can we predict aCH without using absorption bands associated with it?
Hypothesis:
  Mass is explained by several polyfunctional molecules.
  We are able to predict aCH and other mass in the same polyfunctional molecule by their association with carbonyl.
Results
8/11

## Slide 24: Prediction of aCH in polyfunctional compounds (laboratory standards)
12-Tricosanone (Ketone): 1 carbonyl and 44 CH
Arachidyl dodecanoate (Ester): 1 carbonyl and 62 CH
Suberic acid: 12 carbonyl and 2 CH
Malonic acid: 2 carbonyl 2 CH
Results
9/11

## Slide 25: Prediction of aCH in lab standards
12-Tricosanone (Ketone): 1 carbonyl
44 CH
Arachidyl dodecanoate (Ester):
1 carbonyl
62 CH
Ketone and ester

## Slide 26: Prediction of aCH in lab standards
Suberic acid:
2 carbonyl
12 CH
Malonic acid:
2 carbonyl
2 CH
Dicarboxylic acids

## Slide 27: Prediction of aCH in polyfunctional compounds (laboratory standards)
Results
11/11

## Slide 28: Summary
We predict accurately TOR OC measurements by FTIR spectra of ambient samples collected on Teflon filters (18 sites, 3136 samples).
Predictions based on only 10 wavenumbers (0.5% of the whole spectra) have similar or better performance of model that uses the whole spectra 2784 wavenumbers.
The ElnetPLS model has the potentiality to eliminate uninformative wavelengths that interfere with predictions.
Mass of PM2.5 OM in these samples are dominated by a few polyfunctional molecules.
We are able to predict aCH and other mass in the same polyfunctional molecule by their association with carbonyl.
The 10 wavenumbers selected are in carbonyl region of the spectra and they seems to be informative enough to predict masses from different compounds.
Summary
1

## Slide 29: Presentations
O45-BAP-AC-17: Computational tools for functional group analysis of organic aerosols.
  Friday 09/09/2016 14:40, Room 3
P3-BAP-AC-007 An Automated Baseline Correction Method for Atmospheric Aerosol Infrared Spectra Collected on Polytetrafluoroethylene (Teflon) Filters.
  Thursday 08/09/2016. Poster session: Basic Aerosol Processes - Aerosol Chemistry.
Thank you

## Slide 30: Prediction of aCH in polyfunctional compounds (laboratory standards)
12-Tricosanone (Ketone): 1 carbonyl and 44 CH
Arachidyl dodecanoate (Ester): 1 carbonyl and 62 CH
Suberic acid: 2 carbonyl and 2 CH
Malonic acid: 2 carbonyl 2 CH
Results
10/11

## Slide 31: Lab standards – aCH – Parrcoord Plot

## Slide 32: 10 wavenumbers  simpler interpretation
Shurvell, H.: Spectra–Structure Correlations in the Mid-and Far-Infrared, Handbook of vibrational spectroscopy, 2002

## Slide 33: TOR OC prediction – Rural Samples
Results
1/2

## Slide 34: TOR OC prediction – Urban Samples
Results
1/2

## Slide 35: TOR OC prediction – 14 wavenumbers model
Results
1/2