## Slide 1
Surface Clutter Suppression Experiment using P-band Multi-Channel SAR Ice Sounder Data over Jutulstraumen Glacier
C.C. Lin1, D. Bekaert1, N. Gebert1, T. Casal1, J. Dall2, A. Kusk2, S.S. Kristensen2, R. Forsberg2, J. Mosig3, and J.-F. Zürcher3
1) European Space Agency (ESTEC), Keplerlaan 1, 2200 AG Noordwijk, The Netherlands (Chung-Chi.Lin@esa.int)
2) Technical University of Denmark, 2800 Kongens Lyngby, Denmark
3) Swiss Federal Institute of Technology, 1015 Lausanne, Switzerland
ABSTRACT
In the context of a possible future satellite ice sounding mission, surface clutters are expected to severely hamper measurement of weak radar echoes from the depth due to the unfavourable observation geometry. Synthetic aperture radar (SAR) processing enables to attenuate surface clutters in the forward and backward directions, but not in the across-track directions. Thus, additional across-track clutter cancellation is a necessary step for extracting subsurface radar echoes masked by strong surface clutters. ESA’s P-band POLarimetric Airborne Radar Ice Sounder (POLARIS), recently upgraded with a larger antenna of 4 m length, enables simultaneous reception of up to 4 sub-aperture channels in across-track. Several experimental datasets were acquired in the multi-channel configuration over East Antarctica during the Danish IceGrav campaign in Feb. 2011.
POLARIS Instrument:
Built and flown by Technical University of Denmark
Key parameters: P-band 435 MHz (  69 cm)
  Bandwidths 6 - 85 MHz
  4- & 8-element antennas
  Phase-centres: 4
  Carrier: Twin Otter (Air Greenland) & Basler DC-3 (Ken Borek)
1
2
2
4
3
3
4
1
Backscattered wave
POLARIS radar electronics
Ch-1
Ch-2
Ch-3
Ch-4
POLARIS antenna
Complex baseband dig. signals
SAR focusing
SAR focusing
SAR focusing
SAR focusing
Range comp. & SAR proc.
W1
W2
W3
W4

Surface clutter suppression
(Wi’s are functions of time)
Ref: J.R. Guerci, “Space-Time Adaptive Processing”
Surface clutter
Surface clutter
(1) Beam-steering: Steering the beam towards the optimum sounding direction
- Maximise the desired signal
- Surface clutters are present in the angular ranges where the two-way antenna gain is significant
(2) Null-steering: Continuously steer the pattern-nulls towards the direction-of-arrivals of the surface clutters
- Minimise the surface clutters
- Sufficient gain towards the direction of the desired signal is not always ensured
Surface clutter
Surface clutter
Example of null-steering synthesis
(3) Optimum beam-forming = Beam-steering + null-steering
Continuous pattern optimisation, i.e. optimisation of the weighting coefficients Wi’s so as to:
- Maximise the signal-to-noise ratio (SNR)
- Maximise the signal-to-clutter ratio (SCR)
POLARIS has 4 degrees of freedom
 Up to 3 nulls can be generated
POLARIS phase-centers are spaced 1.4  apart
 Grating lobes are present
Example of optimum beam-forming
POLARIS antenna
Digital beam-forming technique
Example of optimum beam-forming synthesis
IceGrav Campaign 2011 in East Antarctica:
The IceGrav project is a close scientific collaboration between Tech. Univ. Denmark, Nat. Geosp.-Intel. Agency, Univ. of Texas, Univ. of Bergen/NPI/Norway, IAA/Argentina and Brit. Antarctic Survey/UK. The primary goal is to measure airborne gravity in hitherto unmapped areas, and eventually contribute to a coordinated Antarctic gravity grid compilation, for basic use in geodesy, geophysics, and satellite orbit determination. The secondary goal is to provide basic radar, laser and magnetic data, as made possible by the rather large long-range DC-3 aircraft.
Surface echo
Double bounce surface echo
Ice bottom
POLARIS coastal flight path
Cross-section of Jutulstraumen glacier
Coastal flights
Before clutter suppression
(across-flow profile)
After clutter suppression
Before clutter suppression
(along-flow profile)
After clutter suppression
Conclusion:
The multi-phase-center capability of POLARIS was tested for the first time over the Jutulstraumen glacier in Feb. 2011. An optimum beam-former processing for POLARIS was developed and used to validate its enhanced functionality and technique for clutter suppression. A successful application of the technique has been demonstrated with an attenuation of the off-nadir clutter power of up to 10 dB. The optimum beam-forming algorithm is sensitive to the surface scattering model used to estimate the clutter power, as its relative importance with respect to the instrument thermal noise must be known a priori.