## Slide 1: Markers for risk to develop atrial fibrillation based on a new electrocardiographic tool Alain Viso1, Marta Aceña2, Remo Leber3, Aline Cabasson4, Roger Abächerli3, Lukas Kappenberger5, Angelo Auricchio2, Jean-Marc Vesin1 1École Polytechnique Fédérale de Lausanne, 2Cardiocentro Ticino, 3SCHILLER AG, 4Université Nice Sophia Antipolis, 5Lausanne Heart Group, Lausanne, Switzerland
Goal
Early recognition of patients prone to atrial fibrillation
Analysis of P wave features on lead V1 during sinus rhythm
Method
Analysis of 68 ECGs 5 minutes long recorded in sinus rhythm and at sampling frequency of 1 KHZ was performed
48 from group A are healthy patients aged between 45 and 75
6 from group B are healthy patients aged between 75 and 85
29 from group D are patients with history of AF aged between 48 to 72 (prone to AF)
Preprocessing
Baseline drift was removed by means of median filters
R waves were detected using a threshold technique
P waves were searched in a window of 200 ms starting 300 ms before the R wave.
P onsets and ends were obtained using first and second derivative estimates
P wave features extracted on V1
  P onset
  P wave offset
  P width (P onset – end of P wave)
Results
Measurements | Group A | Group B | Group D
Heart rate (bpm) | 61 ± 9 | 58 ± 4 | 62 ± 10
P wave duration (ms) | 124 ± 18 | 132 ± 17 | 131 ± 25
P-R interval (ms) | 200 ± 22 | 230 ± 30 | 209 ± 49
Variance of the beat-to-beat Euclidean distance | 0.22 ± 0.09 | 0.31 ± 0.20 | 0.42 ± 0.22
Summary of the results
Using P-R interval and the P width features, no significant differences between the groups were obtained
The variance of the beat-to-beat P-wave Euclidean distance was higher for the group D than for the other two groups (p<0.001). This may be indicative of disturbed conduction in the atrial tissue leading to differences in the electrical pathway used by the P-wave
Plotting the square root of the mean vs square root of the variance of the Euclidean distance we can identify 2 different clusters between healthy and prone to AF subjects
  P-R interval (P onset – peak of R wave)
  Euclidean distance between beat-to-beat resynchronized P waves
Conclusion
This study provides a valuable marker (beat-to-beat Euclidean distance) to perform a good detection of people prone to AF