## Slide 1: Transport regimes for fast ions in TORPEX toroidal magnetized plasmas
Ivo Furno
F. Avino, A. Bovet, A. Fasoli
K. Gustafson, P. Ricci
Centre de Recherches en Physique des Plasmas, Switzerland
H. Boehmer, W. Heidbrink, S. Zhou
University of California Irvine, USA
13th IAEA Technical Meeting on Energetic Particles in Magnetic Confinement Systems, Beijing, 2013

## Slide 2: Outline
  Motivations
  The TORPEX device and the diagnostics
  ideal interchange turbulence
  fast ions source and detector
Experimental measurements
  fast ion transport: energy dependence
Theoretical framework
  Fluid simulations
Comparison simulations – experiments
Transport regimes for fast ions
Outlook and conclusions

## Slide 3: Outline
  Motivations
  The TORPEX device and the diagnostics
  ideal interchange turbulence
  fast ions source and detector
Experimental measurements
  fast ion transport: energy dependence
Theoretical framework
  Fluid simulations
Comparison simulations – experiments
Transport regimes for fast ions
Outlook and conclusions

## Slide 4: Why study fast ion transport by turbulence in simple devices?
Fast particles and turbulence are pervasive in Nature and laboratory:
in magnetic fusion devices: a-particles and beam-ion confinement are important for ITER and next step devices.
Basic plasma physics devices allow simpler investigations:
many details of turbulence and fast ions are directly measured
key experimental physics parameters can be varied systematically
direct comparison with numerical simulations  code validation

## Slide 5: A definition of transport regimes
Spreading in time of the particle positions to extract an exponent:
K. Gustafson et al, PoP 2012
time
variance
g < 1 “sub-diffusive”
g > 1 “super-diffusive”
Are all these regimes accessible to fast ions?
Which key elements determine the regime?
Diffusive  s2=Dt1

## Slide 6: Outline
  Motivations
  The TORPEX device and the diagnostics
  ideal interchange turbulence
  fast ions source and detector
Experimental measurements
  fast ion transport: energy dependence
Theoretical framework
  Fluid simulations
  Transport regimes for fast ions
Comparison simulations – experiments
Outlook and conclusions

## Slide 7: TORPEX (TORoidal Plasma EXperiment) at CRPP
major radius = 1m, minor radius = 20cm
Magnetron
for plasma
production
28 toroidal field coils
4 vertical field coils

## Slide 8: TORPEX and the simple magnetized torus (SMT)

## Slide 9: TORPEX and the simple magnetized torus (SMT)
Bt~800Gauss
Toroidal coils

## Slide 10: TORPEX and the simple magnetized torus (SMT)
Bt~800Gauss
Toroidal coils
Bv~10Gauss
Vertical coils

## Slide 11: TORPEX and the simple magnetized torus (SMT)
Helical field lines winding N times around the torus
B and curvature  interchange drive
Open field lines

## Slide 12
Ideal Interchange
Resistive Interchange
Drift
k|| =0
Interchange drive not
effective
At low N, SMTs are dominated by field-aligned turbulence
N~2  k|| =0, ideal interchange turb.
Te~5-10eV, Ti<<Te
ne~3x1016m-3
P. Ricci and B. Rogers, PRL 2010
inverse pressure gradient
Notes: 12

## Slide 13
Blob region
Interchange wave
High field side
Low field side
Ideal interchange turbulence: waves and blobs
I. Furno et al., PRL 2008, 2011; C. Theiler et al., PRL 2009, 2012

## Slide 14: Ideal interchange regime: waves and blobs
High field side
Low field side

## Slide 15: Source + GEA  3D fast ion profiles

## Slide 16
Miniaturized 6Li+ ion source – Collaboration with UCI
Thermo-ionic effect (~1200o)
Ion current ~ 10μA
Alumino-silicate coating
6Li doping
Heating wires (30W)
Tungsten body
Emitter
1 cm
BN casing
Extract. grid
Acc. grid
Compact, vacuum and plasma safe BN casing
Double grid accelerating scheme
Geometry optimized for small beam divergence
Extraction voltage: ~10V–1kV  E fast ion =10eV-1keV

## Slide 17
The source is installed on a toroidally moving system
Fast ion source  quasi-parallel injection (~5 deg), spreading ~10 deg
Toroidal moving
system
36mm
TORPEX
vacuum vessel

## Slide 18
The fast ion detector: double gridded-energy analyzer
First grid
Second grid – electron rejection
Collector – ion selector
8 mm
Fast ion beam
G. Plyuschev et al., RSI 2006

## Slide 19
radial
poloidal
GEA detector
TORPEX
vacuum vessel
A 2D movable system allows poloidal measurements

## Slide 20
GEA detector
TORPEX
vacuum vessel
A 2D movable system allows poloidal measurements
x
y

## Slide 21: Synchronous detection for small signals
Small fast ion
current < 1mA
Source ON
Source OFF
Synchronous detection
Large SN ratio over 10s
time
A. Bovet et al., submitted to PPCF
Generate a CW plasma

## Slide 22: Outline
  Motivations
  The TORPEX device and the diagnostics
  ideal interchange turbulence
  fast ions source and detector
Experimental measurements
  fast ion transport: energy dependence
Theoretical framework
  Fluid simulations
Comparison simulations – experiments
Transport regimes for fast ions
Outlook and conclusions

## Slide 23: Measurements at two fast ion energies
Distance from the source = 0.2 m
E = 70 eV
E/Te ≈ 46
source
detector
Fast ion injection location

## Slide 24: Measurements at two fast ion energies
Distance from the source = 0.2 m
E = 70 eV
E/Te ≈ 46
source
detector
Fast ion injection location
E = 30 eV
E/Te ≈ 20

## Slide 25: Measurements are performed at two energies
E = 70 eV
E = 30 eV
E/Te ≈ 46
E/Te ≈ 20
Distance from the source = 2.2 m
detector
source

## Slide 26: Different radial spreadings are observed for the two energies
Exp. E = 70 eV
Exp. E = 30 eV
Radial variance of the beam

## Slide 27: Outline
  Motivations
  The TORPEX device and the diagnostics
  ideal interchange turbulence
  fast ions source and detector
Experimental measurements
  fast ion transport: energy dependence
Theoretical framework
  Fluid simulations
Comparison simulations – experiments
Transport regimes for fast ions
Outlook and conclusions

## Slide 28: The Global Braginskii Solver (GBS) code models TORPEX plasmas
ρi << L,  << 1
ω << Ωci
Braginskii model
Electrostatic
Drift-reduced Braginskii equations
Collisional
Plasma
Parallel dynamics
Magnetic curvature
Source
Diffusion
Convection
+ similar equations for Te, Ω (vorticity= )
+ parallel momentum balance for V||e, V||i
P. Ricci et al., PoP 2009, 2011
3D global, full code, however it is used in the 2D version since k//=0

## Slide 29: 3D turbulent fields are constructed from 2D simulations
Fast ions (~105 particles) are injected in the turbulent electric field.
Trajectories are computed by solving the full equation of motion

## Slide 30: Full time dynamics of the fast ions is obtained
K. Gustafson et al, Phys. Plasmas (2012)

## Slide 31: Synthetic profiles are reconstructed from simulations
E = 70 eV
E = 30 eV
Toroidal position

## Slide 32: Simulations and experiments are in good agreement
Exp. E = 70 eV
Exp. E = 30 eV
Synthetic diagnostic 70 eV
Synthetic diagnostic 30 eV

## Slide 33: Outline
  Motivations
  The TORPEX device and the diagnostics
  ideal interchange turbulence
  fast ions source and detector
Experimental measurements
  fast ion transport: energy dependence
Theoretical framework
  Fluid simulations
Comparison simulations – experiments
Transport regimes for fast ions
Outlook and conclusions

## Slide 34: Transport is characterized by the radial variance

## Slide 35: Different transport regimes are revealed
E = 70 eV
E = 30 eV
gR~1.3
“super-diffusive”
gR~0.38
“sub-diffusive”

## Slide 36: A look at trajectories suggests mechanisms for reducing transport
E = 20 EV
E = 70 EV
Parallel injection
E= 70 EV
45 deg. injection

## Slide 37: Gyro- and drift-averaging can reduce the radial transport
Gyroaveraging: large Larmor orbits smooth out electrostatic turbulence
kperp r~2
Drift-orbit averaging: vertical motions smooth out electrostatic turbulence
tx\ty~5
K. Gustafson et al, PRL 2012

## Slide 38: Transport regime is determined by E/Te and turbulence amplitude
kperp r~2
Gyroaveraging
condition
Drift-averaging
condition
Normalized energy (E/Te)
Normalized fluctuations
amplitude (eF/Te)
tx/ty ~ 5

## Slide 39: Outline
  Motivations
  The TORPEX device and the diagnostics
  ideal interchange turbulence
  fast ions source and detector
Experimental measurements
  fast ion transport: energy dependence
Theoretical framework
  Fluid simulations
Comparison simulations – experiments
Transport regimes for fast ions
Outlook and conclusions

## Slide 40: SMTs have similarities with tokamak SOLs
Scrape-Off Layer
open field lines
B and curvature
Plasma current
Last Closed Flux Surface
magnetic topology change

## Slide 41: TORPEX 2013 and beyond (just getting started)
Current
1kA-10V supply; flat top ~1s, Iconductor~1kA; ~100 discharges/day

## Slide 42: New exciting possibilities to study fast ion physics
Confined plasmas
Alfven wave
Snowflakes
X-point physics
Ripple, 3D, ergodic fields

## Slide 43: Conclusions
  Simple plasma devices, such as TORPEX, offer great possibilities to investigate the fundamentals of fast ion – turbulence physics.
On TORPEX, numerical simulations and experiments reveal that different regimes for fast ion transport are possible depending on their energy and turbulence amplitude.
Gyro- and drift-averaging can effectively reduce turbulent transport.
Upcoming TORPEX experiments will explore more complex magnetic geometries of direct relevance to tokamaks.