## Slide 1: Flat-beam IR optics
José L. Abelleira, PhD candidate EPFL, CERN BE-ABP
Supervised by F. Zimmermann, CERN Beams dep.
Thanks to: O.Domínguez. S Russenchuck, D.Shatilov, M. Zobov
CERN, 22th February 2013
Joint Snowmass-EUCARD/AccNet-HiLumi LHC meeting
Frontier capabilities for Hadron colliders

## Slide 2: Contents
Crab-waists collisions concept
Flat beam optics for LHC
CW for HE-LHC
  Parameters
  Time evolution
Conclusions

## Slide 3: Crab-waist collisions (I)
An important limitation in hadron machines is beam-beam tune shift
A Large Piwinski Angle Φ (LPA)
reduces tune shift, allowing N↑
reduces the length of the collision section, allowing ↓
More luminosity
Length of the Collision section
With Head-on collisions or small φ
But in LPA regime
!
1cm
For LHC

## Slide 4: Crab-waist collisions (II)
Suppressed by crab-waist scheme
On the other hand, a LPA induces strong X-Y resonances
Normal collision scheme
Crab-waist collision scheme
P.Raimondi, D.Shatilov,
M. Zobov
σx*/σy*≥10
Suitable for lepton machines
More challenging for hadron colliders
(2n+1)
Condition for cw collisions
2 sextupoles spaced from the IP
βx*/βy*≥100

## Slide 5: Flat beam optics for LHC
Local chromatic correction in both planes + crab-waist collisions
sext1
sext5
sext3
Chromatic correction
βx*=1.5 m
βy*=1.5 cm
 | Δμx | Δμy
sext1 |  | 
sext2 |  | 
sext3 |  | 
sext4 |  | 
sext5 |  | 
π/2
π/2
π/2
3π/2
3π/2
3π/2
3π/2
2π
5π/2
sext2
sext4
CRAB-WAIST SEXTUPOLE
π/2
The extremely low asks
for a symmetric optics in the IR
Phase advance from IP
Separation magnets

## Slide 6: Flat beam optics for LHC
45 mm
15σy
15σx
σx/ σy=10
Minimum required according to beam-beam simulations.
Reference orbit

## Slide 7: Crab-waist simulations
CW = 0
CW = 0.5
Resonances
Frequency Map Analysis (FMA)
Effective for the beam-beam resonance suppression.
Plot shown for θc = 1.5 mrad
Dmitry Shatilov
Mikhail Zobov

## Slide 8: Luminosity evolution
During a run, N(t) ↓
But there is a significant decrease in, σx*, σy*, and in !
With low , the limitation in the beam-beam tune shift
obliges to introduce blow-up (longitudinal/horizontal).
With large the limitation is almost suppressed.
Beam lifetime due to burn off
LPA allows a bigger for the same Contribution to
  Higher LINT
↘we just have to adjust the parameters to have SR damping as a compensator for the burn off

## Slide 9: Symmetric optics
The lower * allowed by the LPA creates a large beam divergence
-> last quadrupole must be defocusing for the four cases: b1l, b1r, b2l, b2r.
In order to implement a symmetric optics in the IR, two options are proposed for the HE-LHC:
  =2mrad. Use a double-half quadrupole, like in c-w LHC
  =8mrad. Use a double aperture quadrupole with opposite sign.
IR optics is symmetric. Two options
  Match the sym. IR optics to the antisymetric arc optics.
  Design a symmetric optics in the arcs.
N
N
S
S
N
N
S
S
N
N
S
S

## Slide 10: Last quadrupole. =2 mrad
B0=-5.8 T
g=115 T/m
Double half
quadrupole
By(x)
proposed for c-w LHC as a solution to have diff pol quadrupoles for the 2 beams in a same aperture
S. Russenchuck

## Slide 11: Last quadrupole. =8 mrad
Gradient : 220 T/m
By(x)
Double aperture magnets with same polarity (as in LHC arc quadrupoles)
Double aperture magnets with same polarity for c-w HE-LHC
S. Russenchuck
18.4 cm
Gradient : 219 T/m

## Slide 12: Parameters (I)
c.m. energy [TeV] | 33
Circumference [km] | 26.7
Dipole field [T] | 20
Dipole coil aperture [mm] | 40
Beam half aperture [mm] | 13
Injection energy [TeV] | >1.0
Initial longitudinal emittance [eVs] | 5.67
r.m.s. bunch length [cm] | 7.7
peak luminosity [cm-2 s-1 ] | 
c.m. energy [TeV] | 33
Circumference [km] | 26.7
Dipole field [T] | 20
Dipole coil aperture [mm] | 40
Beam half aperture [mm] | 13
Injection energy [TeV] | >1.0
Initial longitudinal emittance [eVs] | 5.67
r.m.s. bunch length [cm] | 7.7
peak luminosity [cm-2 s-1 ] | 
Due to the fast emittance shrink
Initial luminosity ≠ peak luminosity
The initial beam size has been chosen to allow c-w from the beginning of a run
σx*/σy*=10
O. Domínguez.
HE-LHC/VHE-LHC parameters,
time evolutions & integrated luminosities. This workshop

## Slide 13: Parameters (II)
 | θ = 2 mrad | θ = 8 mrad
initial luminosity [cm-2 s-1] | 2.3 | 
N0 [1011] | 2.45 | 3.05
Crossing angle [mrad] | 2 | 8
Technology for last quad. | Double-half quad. | Double aperture quad.
IP beta function (H/V) [m] | 3/0.03 | 
Norm. initial emittance (H/V) [μm rad] | 2.1 | 
Initial beam size IP [μm] | 19/1.9 | 
Number of bunches | 1404 | 
Crossing scheme | horizontal at the two IP | 
Initial Piwinski angle | 4.1 | 16.3
Initial total tune shifts [10-3] | 3.2/1.3 | 0.3/0.4
maximum total tune shifts | 8.9/2.4 | 1.1/1.2
Beam separation [σ] | 317 | 12680
 | θ = 2 mrad | θ = 8 mrad
initial luminosity [cm-2 s-1] |  | 
N0 [1011] | 2.45 | 3.05
Crossing angle [mrad] | 2 | 8
Technology for last quad. | Double-half quad. | Double aperture quad.
IP beta function (H/V) [m] | 3/0.03 | 
Norm. initial emittance (H/V) [μm rad] | 2.1 | 
Initial beam size IP [μm] | 19/1.9 | 
Number of bunches | 1404 | 
Crossing scheme | horizontal at the two IP | 
Initial Piwinski angle | 4.1 | 16.3
Initial total tune shifts [10-3] | 3.2/1.3 | 0.3/0.4
maximum total tune shifts | 8.9/2.4 | 1.1/1.2
Beam separation [σ] | 317 | 12680
O. Domínguez.

## Slide 14: Parameters (III)
 | θ = 2 mrad | θ = 8 mrad
Long. SR emittance damping time [h] | 1.01 | 
Transverse SR emittance damping time [h] | 2.02 | 
Initial horizontal IBS emittance rise time [h] | 37.51 | 21.1
Initial vertical IBS emittance rise time [h] | 72.02 | 42.2
Initial longitudinal IBS rise time [h] | 72.45 | 40.7
Beam intensity lifetime [h] | 14.6 | 29.9
Optimum run time [h] | 6 | 8.5
Opt. av. Int. luminosity/day [fb-1] | 1.63 | 1.93
O. Domínguez.

## Slide 15: Time evolution. =2 mrad
emittance
Total tune shifts
Beam size ratio
Long. Beam size
Piwinski angle
Far below 0.01
C-w condition
Transverse beam sizes
Luminosity
O. Domínguez.

## Slide 16: Time evolution. =8 mrad
emittance
Total tune shifts
Long. Beam size
Piwinski angle
Transverse beam sizes
Luminosity
Even far below 0.01
O. Domínguez.
Beam size ratio

## Slide 17: Luminosity evolution
O. Domínguez.

## Slide 18: Conclusions
An extremely-flat beam optics (βy*/βy*=100) is conceptual possible for LHC and HELHC
  Large Piwinski angle, to reduce the collision area and allow for a lower βy*
  Local chromatic correction
  Possibility to have crab waist collisions that can increase luminosity and suppress resonances
  Can accept higher brightness.
  Significant increase in Lint
With crab-waist collisions there is no tune shift limitation: no need for emittance blow up.
  LPA allows for a higher brightness: increases beam lifetime
  SR damping for the three planes increases luminosity

## Slide 19: Thank you…
…For your attention