## Slide 1: Effects of plasma shaping on MHD and electron heat conductivity; impact on alpha electron heating
O. Sauter for the TCV team
Ecole Polytechnique Fédérale de Lausanne (EPFL)
Centre de Recherches en Physiques des Plasmas (CRPP)
Lausanne, Switzerland

## Slide 2: Outline
Introduction
Elongation and triangularity on internal kink
Shape effects on ELMs
Triangularity effects on transport
Negative triangularity for DEMO?

## Slide 3: Introduction
This is a short and rapid survey of some published TCV results related to the effects of plasma shape
Studies on sawteeth => effects of shape on internal kink / core MHD stability
Studies on ELMs => effects of shape on edge stability
Studies on transport => effects of shape on micro-stab.
Full list of references given at end of the talk

## Slide 4: Reminder: bN limit and elongation
Troyon limit:
Ip
bN*Ip
b
q95=2
TCV design: bN decreases for k>2.5 before q95=2
TCV results: bN does decreases for k>2.2 before q95=2
A. Turnbull et al, Nucl. Fus. 28 (1988) 1381
F. Hofmann et al, PRL 81 (1998) 2918

## Slide 5: Sawteeth and plasma shape
k and d do not penetrate so much into plasma center
yet, large effects of shape on sawteeth
Reimerdes et al, PPCF 42 (2000) 629: Effect of triangular and elongated plasma shape on the sawtooth stability
Same shape dependence: Mercier, ideal internal kink, sawtooth period

## Slide 6
Ideal Internal Kink Mode
Analytical expression used [Graves PPCF (2005), Martynov PPCF (2005)]:

## Slide 7: Sawteeth «disappear» at high elongation
Can avoid sawteeth by:
Full stabilization (lengthen sawtooth period -> ∞)
Full destabilization (shorten ST period -> 0)
Reimerdes et al, PPCF 48 (2006) 1621: Sawtooth behaviour in highly elongated TCV plasmas

## Slide 8: «continuous sawteeth» = nonlinear sat. MHD
3D displacement of nonlinar saturated MHD can be predicted
helical core of «hybrid» type plasmas ~ new 3D equilibrium
Graves et al, PPCF 55 (2013) 014005: Magnetohydrodynamic helical structures in nominally axisymmetric low-shear tokamak plasmas

## Slide 9: n=1 growth rate well known from ideal MHD
g and tST have same dependence on d
Best fits of g(n=1) do not need d in the formulas
k decreases rapidly towards center at high d => main effect of d on internal kink through effective value of k1
Martynov et al, PPCF 47 (2005) 1743: The stability of the ideal internal kink mode in realistic tokamak geometry
At high k, small shear:

## Slide 10: ELMs at negative d
Significant effect of d on ELM frequency observed in TCV ohmic H-modes
Pochelon et al, PFR 7 (2012) 2502148: Recent TCV Results – Innovative Plasma Shaping to Improve Plasma Properties and Insight

## Slide 11: ELMs at negative d: main effect on high n
No «2nd stability» effects
More unstable
Smaller ELMs
Medvedev et al, NF (2015): Negative triangularity tokamak: stability limits and
perspectives as fusion energy system

## Slide 12: Transport: better e- confinement at negative d
Camenen et al, NF 47 (2007) 510: Impact of plasma triangularity and collisionality on electron heat transport in TCV L-mode plasmas
Same profiles at half the power ! Factor 2 confinement improvement

## Slide 13: Transport: better e- confinement at negative d
Camenen et al, NF 47 (2007) 510: Impact of plasma triangularity and collisionality on electron heat transport in TCV L-mode plasmas

## Slide 14: Nonlinear gyrokinetic simulations at d<0
Marinoni et al, NF 51 (2009) 055016: The effect of plasma triangularity on turbulent transport: modeling TCV experiments by linear and non-linear gyrokinetic simulations
Ratio of ce between positive over negative d can be explained outside r=0.7
Clear difference in the core

## Slide 15: On core stiffness and edge non-stiffness
Sauter et al, PoP 21 (2014) 055906: On the non-stiffness of edge transport in L-mode tokamak plasmas
Linear with rv in edge region
Gradient increasing with Ip (P, nel, …)
Can better relate with gyrokinetic simulations
Can better extract main parameters’ variations
From data
From educated fit

## Slide 16: Role of edge for d effects on transport
Sauter et al, PoP 21 (2014) 055906: On the non-stiffness of edge transport in L-mode tokamak plasmas
Same input power with positive and negative d with good radial resolution
Almost whole profile self-similar…except edge (next VG)

## Slide 17: Role of edge for d effects on transport
Sauter et al, PoP 21 (2014) 055906: On the non-stiffness of edge transport in L-mode tokamak plasmas
Te(rv=0.8) increases with negative d because of increased gradient in edge region 0.8-1.0
Consistent with previous simulations (Marinoni et al)

## Slide 18: Role of d revisited with gyrokinetic
Merlo et al, PPCF (2015): Investigating profile stiffness and critical gradients
in shaped TCV using local gyrokinetic simulations of turbulent transport
No change in core
d<0 better at outer radii
Less stiff near edge
Linear critical gradients seem to play a role
Need global runs
Flux tube GENE

## Slide 19: Ion transport also stiff even in ohmic
Merle et al, IAEA (2014)
Ti versus Ip scan. Same R/LTi across radii and Ip, scales with nel
Ti(0.8) increases with Ip similar to Te. Same with PEC scan
Thus with strong electron heating, expect same behaviour
Expect same behaviour with shaping as Te

## Slide 20: Negative delta, an option for DEMO
Kikuchi et al, 1st International e-Conference on Energies (2014)
Design with heat flux handling as main priority (instead of core transport/stability)
Large gain with «R» for divertor, large gain for pumping
Potential gain from controlled ELMs, transport

## Slide 21: References
Turnbull et al NF 28 (1988) 1379, Current and beta limitations for the TCV tokamak
Hofmann et al, PRL 81 (1998) 2918, Exp. and Theor. Stab. Limits of High k Tokamak Plasmas
Reimerdes et al, PPCF 42 (2000) 629: Effect of triangular and elongated plasma shape on the ST stability
Graves et al PPCF 47 (2005) B121, Sawtooth control in fusion plasmas
Martynov et al, PPCF 47 (2005) 1743: stability of the ideal internal kink in realistic tokamak geometry
Reimerdes et al, PPCF 48 (2006) 1621: Sawtooth behaviour in highly elongated TCV plasmas
Graves et al, PPCF 55 (2013) 014005: Magnetohydrodynamic helical structures in nominally axisymmetric low-shear tokamak plasmas
Camenen et al, NF 47 (2007) 510: Impact of plasma triangularity and collisionality on electron heat transport in TCV L-mode plasmas
Marinoni et al, NF 51 (2009) 055016: The effect of plasma triangularity on turbulent transport: modeling TCV experiments by linear and non-linear gyrokinetic simulations
Pochelon et al, PFR 7 (2012) 2502148: Recent TCV Results – Innovative Plasma Shaping to Improve Plasma Properties and Insight
Sauter et al, PoP 21 (2014) 055906: On the non-stiffness of edge transport in L-mode tokamak plasmas
Merle et al, IAEA (2014), EX/P3-55, From Edge Non-Stiffness to Improved IN-Mode: a New Perspective on Global Tokamak Radial Transport
Merlo et al, PPCF (2015) May: Investigating profile stiffness and critical gradients in shaped TCV using local gyrokinetic simulations of turbulent transport
Medvedev et al, NF (2015): Negative triangularity tokamak: stability limits and perspectives as fusion energy system
Kikuchi et al, 1st International e-Conference on Energies (2014)

## Slide 22
Back-up

## Slide 23: Role of edge for d effects on transport
Sauter et al, PoP 21 (2014) 055906: On the non-stiffness of edge transport in L-mode tokamak plasmas
Te and ne edge gradient increase with Ip, P, nel, d<0