## Slide 1: Experimental assessment of active electroacoustic absorbers for broadband room modes damping
Dr. Hervé Lissek, Dr. Sami Karkar, Etienne Rivet (EPFL)
Dr. Véronique Adam, Torje Thorse, Quentin Berthet (Goldmund)
Prof. Antoine Pittet, David Strobino (HEPIA)
Alain Roux, Christian Martin (PSI Audio)

## Slide 2: Outline
Context: room modes in the low-frequency range
Presentation of the Electroacoustic Absorber prototype
Experimental assessment: modal damping in rooms

## Slide 3: Context

## Slide 4: Context
Room modes characterization: standing waves
   uneven spatial distribution of sound energy

## Slide 5: Context
Room modes characterization: frequency response
  dominated by strong peaks (resonances) and dips (anti-resonances)

## Slide 6: Context
Room modes characterization: modal decay time
   sustain at the various resonance frequencies once the source stops
   definition of MT60 (see RT60) – may strongly vary with frequency

## Slide 7: Problem(s)
Low-frequency noise issue

## Slide 8: Problem(s)
Music rendering issue in the low-frequency range

## Slide 9: Problem(s)
State of the art sound absorbers
totally inefficient in the LF range (see /4 rule)
Porous materials
Helmholtz resonators
Panel absorbers
absorption
BF

## Slide 10: Problem(s)
State of the art sound absorbers
bass-traps (membrane absorbers)
Efficient LF narrow-band (1 resonance frequency) sound absorbers
e-traps (active bass traps)
Efficient on 2 (adjustable) resonance frequencies
E-trap

## Slide 11: Electroacoustic Absorbers

## Slide 12: Electroacoustic absorbers
Development of an active sound absorption solution with >0.83 along the range [20 - 200Hz]
Based on actuated membranes (loudspeakers) used as a membrane absorbers
Evaluation in reverberant conditions, focusing on low-frequency sound «equalization»
H. Lissek, R. Boulandet, and R. Fleury, “Electroacoustic absorbers: bridging the gap between shunt loudspeakers and active sound absorption”, J. Acoust. Soc. Am., 129(5), 2968-2978, (2011).

## Slide 13: Electroacoustic absorbers
Parameter | Description | Value | Unit
Mms | Moving mass | 14.7 | g
Rms | Mechanical resistance | 1.31 | N.s.m-1
Cms | Mechanical compliance | 242.3 | mm.N-1
Sd | Membrane surface | 151 | cm2
Bl | Force factor | 6.85 | N.A-1
Vb | Cabinet volume | 10 | dm3
r | Air mass density | 1.2 | kg/m3
c | Sound celerity in air | 344 | m.s-1
pt
v

## Slide 14: Electroacoustic absorbers
A desired acoustic impedance Zat can be assigned by identifying the controller transfer function:
pt
v

## Slide 15: Electroacoustic absorbers
Implementation in the prototype
CompactRIO® real-time controller
Voltage-driven current amplifier

## Slide 16: Electroacoustic absorbers
ISO 10534-2 : acoustic impedance measurement technique
Acoustic impedance
Absorption coefficient

## Slide 17: Experimental validation of room modes damping

## Slide 18: Experimental assessment
4x4 electroacoustic absorbers prototypes
(total surface = 16x151 cm2 = 0.24 m2)
In a reverberant chamber of 226.9 m2
 evaluation of room modal damping

## Slide 19: Experimental assessment
Frequency response without and with absorbers
   identify individual room modes
   assess damping performance on peaks and dips amplitudes
Modal decay times without and with absorbers
   assess damping performance in the time domain
Recording of music rendering, without and with absorbers
   listen to the effect on music rendering
Recording of kick drum, without and with absorbers
   listen to the effect on acoustic music playing

## Slide 20: Experimental setup
Hardware
Recorders/analyzers
  B&K Pulse (frequency responses)
    frequency resolution: 31.5 mHz
  M-Audio M-Track 8 soundcard (recordings)
Microphones
Sources
Facility (reverberant chamber, V=215.6 m3, S=226.9 m2)
  Subwoofer
  Kick drum
  (Pearl Export)
  PCB 130D20
  (frequency responses)
  Beyerdynamic M101 N
  (recordings)
Supplementary
panel absorber
4 electroacoustic absorbers
at the 4 room corners
7 microphone positions

## Slide 21: 1. Frequency response
(blue: «Hardwalls», red: «Absorbers»)

## Slide 22: 1. Frequency response
Modal damping (dB)

## Slide 23: 2. Modal decay time
Mode 8 – waveforms
(hardwalls : 52.78 Hz - absorbers : 52.72 Hz)
Mode 8 - echograms
(hardwalls : 52.78 Hz - absorbers : 52.72 Hz)

## Slide 24: 2. Modal decay time
1/6MT10
1/3MT20
1/2MT30

## Slide 25: 2. Modal decay time

## Slide 26: 2. Modal decay time

## Slide 27: 3. Music rendering
Peggy Lee «Fever»
White Stripes «7 nation army»
What’s this tune?
What’s this tune?

## Slide 28: 4. Kick drum
Waveforms
Echograms

## Slide 29: Conclusions and perspectives
4 electroacoustic absorbers prototypes achieve efficient room mode damping in the reverberant chamber
  Max damping: 12.2 dB @ 58 Hz,
  Global damping: 8 dB over [20 – 100 Hz],
  Max modal decay time reduction: 85% @ 58 Hz
  (from 20 s down to 3 s),
for a total absorber surface representing only 0.1% of the whole room walls surface

## Slide 30: Conclusions and perspectives
The objective performances are still to be evaluated in a more conventional listening room
Subjective assessments should also be undertaken (to be done in the coming weeks)

## Slide 31: Thank you for your attention
This work has been supported by the Swiss Commission for Technology and Innovation (CTI), under the project INTERACTS, agreement number: 14220.1 PFNM-NM.
e-mail: herve.lissek@epfl.ch