## Slide 1: Estimation of Organic and Elemental Carbon using FT-IR absorbance spectra from PTFE filters
Matteo Reggente
Giulia Ruggeri
Satoshi Takahama
Swiss Federal Institute of Technology Lausanne
Ann Dillner
University of California, Davis

## Slide 2: Nutshell

## Slide 3: Nutshell
What:
  Alternative approach to measure OC and EC
Why:
  OC and EC are major components of atmospheric PM.
  Typically OC and EC are measured using thermal optical methods (quartz filters).
    destructive and relatively expensive
Aim:
  Reduce the operating costs of large air quality monitoring networks.
  Fourier transform infrared spectra (FT-IR) of ambient PTFE filters
Contributions:
  Accurate predictions
  Anticipation of the prediction error
Nutshell
1

## Slide 4: Methods

## Slide 5: Methods
Methods
1/2
Alternative Approach: PTFE filters + FT-IR + PLS regression
Calibration: Partial Least Square (PLS) regression
The problem for infrared spectra is
underdetermined: few hundred samples × few thousand wavenumbers
multicollinear: serial correlation of absorbances across wavenumbers
Notes: PLS: bilinear decomposition of both X (spectra matrix) and y (response variable vector) onto orthogonal bases.
The two sets of factors are related through a series of weights (columns of W) used to reconstruct factor scores T and regression coefficients b.
Training and selection: number of factors selected by evaluating against a validation set:

## Slide 6: Methods
Methods
2/2
Ambient Samples: IMPROVE network
More than 3000 collocated ambient samples:
PTFE filters and FT-IR spectra
Quartz filters and TOR
2011: 6 + 1 sites; 794 samples
Dillner and Takahama, Atmos. Meas. Tech., 2015a (OC)
Dillner and Takahama, Atmos. Meas. Tech., 2015b (EC)
2013: 6 + 11 sites; 2239 samples
Reggente, Dillner and Takahama submitted AMTD, 2015

## Slide 7: Results

## Slide 8: Results – Test 2011
Results
1/9
Dillner A. M. and Takahama S., AMT, 2015
Dillner A. M. and Takahama S., AMT, 2015

## Slide 9: Results – Test 2013, Sites present in the calibration
Results
2/9
Dillner A. M. and Takahama S., AMT, 2015
Dillner A. M. and Takahama S., AMT, 2015
Reggente et al., submitted AMT, 2015

## Slide 10: Results – Test 2013 Addl, NOT present in the calibration
Results
3/9
Dillner A. M. and Takahama S., AMT, 2015
Dillner A. M. and Takahama S., AMT, 2015
Reggente et al., submitted AMT, 2015

## Slide 11: Results – OC – Test 2013 Addl, NOT present in the calibration
Results
4/9
Can we improve it?
Anticipation of the prediction error
Discrimination between “acceptable” and “unacceptable” predictions
Mahalanobis distance in the feature space (Factor scores of PLS)

## Slide 12: Anticipating prediction error by Mahalanobis distance
Results
5/9
Mahalanobis distance (DM) is the N-D generalization of the standard normal probit.
We calculate multivariate distribution parameters from PLS scores T of the calibration spectra.
New spectra are projected into this space and DM2 calculated with respect to the calibration spectra without knowledge of OC, EC concentrations
We evaluate our ability to anticipate prediction errors of OC, EC in 4 quadrants:
  TP – true positive
  TN – true negative
  FP – false positive
  FN – false negative

## Slide 13: Results – Anticipating Prediction Error
Results
6/9

## Slide 14: OC - Reducing Prediction Error
Results
7/9
Recalibration leads to lower errors
High Mahalanobis distance sites removed

## Slide 15: EC - Reducing Prediction Error
Results
8/9
Recalibration leads to lower errors
High Mahalanobis distance sites removed
Removing improves
R2 from 0.66 to 0.84

## Slide 16: Sparse calibration models – TOR EC example
N-H bend in amides
Results
9/9
Teflon filter
Strategy:
Use a reduced set of wavenumbers (<10% of original)
Associate wavenumbers with absorption bands
C-C-N, C-N-C bend in amines
benzene ring stretch
ester C-O-C stretch
Why are we able to predict TOR EC with FT-IR?

## Slide 17: Conclusions

## Slide 18: Conclusions
Calibrations can predict OC and EC within TOR precision for sites for which we have calibration samples, and many additional sites
Spectral features allow us to anticipate the prediction error for OC and EC (in most cases) and this can guide us in strategic sample collection and calibration
  room for improving false negative for EC
Sparse methods help us understand what bonds are responsible for our predictions
  aromatic, ester, amide groups common for OC, EC
  carbonyls, alkanes additionally identified for OC
  different vibrational modes for same bonds or functional groups are used
Conclusions
1

## Slide 19: Acknowledgements
Swiss National Science Foundation (200021_143298)
EPFL Founding
IMPROVE program (National Park Service cooperative agreement P++AC91045)
Acknowledgements
1

## Slide 20: Estimation of Organic and Elemental Carbon using FT-IR absorbance spectra from PTFE filters Thank you

## Slide 21: Supplementary Material

## Slide 22: Results – OC – Rural Site
Results
12/17

## Slide 23: Results – OC – Anticipation Prediction Error
Results
13/17
Individual sample, Calibration 2011

## Slide 24: Results – OC – Anticipation Prediction Error
Results
14/17
Individual sample, Test 2011

## Slide 25: Results – OC – Anticipation Prediction Error
Results
15/17
Individual sample, Test 2013

## Slide 26: Results – OC – Anticipation Prediction Error
Results
16/17
Individual sample, Test 2013 Addl

## Slide 27: Results – OC – Anticipation Prediction Error
Results
17/17
Individual sample, Performance

## Slide 28: Results – EC – Rural Site
Results
6/11

## Slide 29: Results – EC – Anticipation Prediction Error
Results
7/11
Individual sample, Calibration 2011

## Slide 30: Results – EC – Anticipation Prediction Error
Results
8/11
Individual sample, Test 2011

## Slide 31: Results – EC – Anticipation Prediction Error
Results
9/11
Individual sample, Test 2013

## Slide 32: Results – EC – Anticipation Prediction Error
Results
10/11
Individual sample, Test 2013 Addl

## Slide 33: Results – EC – Anticipation Prediction Error
Results
11/11
Individual sample, Performance